## Slide 1
MY CERN SUMMER STUDENT
PROGRAMME
Presented by:
Amal Ali Hasan
Supervised by:
Mehmet Ozgur Sahin
& Flavia Cetorelli
Page.1

## Slide 2
Numpy
Matplotlib
uproot
Python
DOCUMENTATIONs
jUPYTER
SWAN
MY CERN PROJECT
Page.10

## Slide 3
WHAT ARE MIPS?
BETHE-BLOCH EQUATION FOR ENERGY LOSS:
valid for heavy charged particles only!
Page.12

## Slide 4
WHAT ARE MIPS?
  all MIPs produce approximately Landau-distributed spectra when traversing the matter
  For each of the heavy charged particles, there exist a particular momentum where the particle is called a “mip”.
  Information about the tracks of the particles can also be extracted from the plot.
Page.13

## Slide 5
PP-COLLISIONS
THINK OF THE PROTON AS A SOUP OF VEGITABLES. IT HAS 3 BROCCOLIES (3 FLAVOUR QUARKS) & FEW OTHER SWIMMING VEGGIES (A SEA OF QUARKS-ANTI QUARKS):
VERTECIES
TRACKS
PILEUP INTRACTIONS
Page.14

## Slide 6
PP-COLLISIONS
IN THE CURRENT RUN OF LHC, THERE ARE MORE THAN ONE HUNDRED BILLION PROTONS IN EACH BUNCH CROSSING!
TWO OPPOSING BUNCHES ARE COLLIDED EACH 25NS!
ONLY 1% OF THE PROTONS THAT COLLIDE ARE CONSIDERED TO BE “IMPORTANT EVENTS”!
IN THIS CHAOTIC SENARIO, THE TRACKS OF ALL HARD COLLISIONS MUST BE ASSIGNED TO THE CORRECT COLLISION VERTEX!
Page.15

## Slide 7
MTD & HL-LHC
THE MIP TIMING DETECTOR (MTD) IS ONE OF THE DEVELOPING DETECTORS FOR THE HIGH LUMINOSITY ERA OF THE LHC (HL-LHC).
INCREASING THE LUMINOSITY OF THE LHC WILL ALLOW US TO:
  STUDY THE PHYSICS BSM,
  MEASURING SELF-COUPLING OF THE HIGGS BOSON,
  TOF MEASUREMENT FOR CHARGED PARTICLES PID
  TRACKING LLP, ETC.
Page.16

## Slide 8
MTD & HL-LHC
  THE 3000 FB-1 INTEGRATED LUMINOSITY OF HL-LHC WILL INCREASE THE NUMBER OF PILE UP INTERACTIONS(FROM 30 TO 140-200).
  THE MTD INTRODUCE THE TIME DIMENSION TO THE VERTEX RECONSTRUCTION TO DISENTANGLE THE INTERACTIONS AND DECREASE THE RATE OF FALSE TRIGGERS.
  THE DETECTOR IS DIVIDED INTO TWO PARTS; THE BARREL TIMING DETECTOR (BTL), AND THE ENDCAP TIMING DETECTOR (ETL).
Page.17

## Slide 9
MTD BTL DETECTOR
  Each azimuthal segment spans 10 degrees having 6 readout units (1 trays).
  In each readout unit there are 12 detector modules.
  In each detector module there are 2 arrays each of 2 TOFHIR chips, 16 LYSO bars and 4 SiPM arrays (each of 16 SiPMs).
  The readout unit has a concentrator card.
Page.18

## Slide 10
WHAT HAPPENS WHEN A MIP TRAVERSE THROUGH A SCINTILATOR ?
MIPs traverse the LYSO cristal emitting photons
Due to the internal reflections of the crystal, photons reach the SiPMs
In the SiPMs, photons are converted to Photoelectrons
The TOFHIR chip is the chip that reads these electrical signals from the SiPMs
The TOFHIR chip is a digitization ASIC specially designed for the MTD BTL detector
Tests showed that optimum time resolution is achieved using the TOFHIR
Page.19

## Slide 11
WHAT IS A TOFHIR CHIP?
  The TOFHIR chip is A low-power, low-noise, Silicon Photomultipliers (SiPM) readout and digitization ASIC specially designed for the MTD BTL detector.
  It is used in the process of timing reconstruction for MTD data acquisition system.
  The design of the chip is derived from the chip used in TOF-PET applications.
  It provides signal amplification, shaping and discrimination for each of 32 independent channels and is radiation tolerant up to 10 Mrad.
Page.20

## Slide 12
LAB MEASUREMENTS
  In this test, an ultraviolet (UV) laser shines either directly on naked SiPMs or on LYSO crystals with attached SiPMs.
  The laser signal is synchronized for both SiPMs (or crystals) that are read out with two TOFHIR readout channels.
  By grouping together the events from different channels when they occur within the same time window (500 ns), the real time of arrival of the MIP can be determined.
Page.21

## Slide 13
raw data conversions/ events coupling/ time precision code
filtering the time information to get only the interesting events indicated by L1-trigger
THE REQUIRED TASK!
Page.22

## Slide 14
What is happening inside the Tofhir chip?
is a current conveyor based on a TIA provides a low impedance input to the sensors output current signal.
Input Pre-amplifier (p)
The input current is then replicated into 3 branches: T, E and QDC blocks. The T and E branches have TIA with configurable gains for baseline
stabilization and noise cancellation.
T, E and qdc branches
Page.23

## Slide 15
t1, t2 and E discriminators
The outputs of TIAS are fed into CFDs for timing measurement
(T1 and T2) and hit selection (E). Each of the discriminators has a threshold (Vth-t1, vth-t2 & vth-e)
In the CFD, the output signal of tia will be added to the inverted and delayed copy of the signal. The result is a bipolar signal with the baseline removed.
What is happening inside the Tofhir chip?
Page.24

## Slide 16
internal trigger logic
The output signals from the cfd are used to control the ASIC internal triggering logic. the events that trigger all the three thresholds are considered valid and digitized.
qdc branch
The QDC measures the integrated charge from the rising edge of trigger Q (generated by the
output of discriminator T2) until the end of the integration window.
The TDC T1 measures the time of the rising edge of trigger T1. The TDC T2 measures the time of the rising edge or falling edge of trigger T2. the adc is analog to digital converter.
tdcs & adc
What is happening inside the Tofhir chip?
Page.25

## Slide 17
Trigger signals involved in the TDC and QDC operation Event packet format
t(coarse): The value of a global clock counter latched on the next clock providing t(coarse).
t(fine): is the digitized voltage stored in CT when the event is valid.
q(coarse): The value of a global counter latched on the next clock after the integration window.
If the event is valid, the charge stored in CQ will be digitized.
TAC-id number: the analog buffer set transmitted along with the event.
What is happening inside the Tofhir chip?
Page.26

## Slide 18
Thank you!